Constrained Least-Squares Linear-Phase FIR Filter Synthesis (CLSLP)
September 28, 2024
William Earl Jones
http://www.wejc.com || wejc@wejc.com
Last Updated 09/28/24 at 13:46

# Introduction
This document describes use of the Constrained Least-Squares Linear-Phase FIR Filter Synthesis Algorithm CLSLP as described in reference [1]. The acronym CLSLP is not used in the technical paper and is only used as a local convenience and as a name for the software package. The acronym LPFIR is used here as an abbreviation for Linear-Phase Finite Impulse Response filter.
# Linear-Phase FIR (LPFIR) Filters
A Linear-Phase FIR filter (LPFIR) is a special form of FIR filter that preserves the timing relationship between signals of different frequencies. Non-Linear phase FIR filters have different phase responses at different frequencies and these errors can accumulate as frequency-dependent time delays in multilayered signal-processing schemes. The linear-phase constraint guarantees that the time delay of different frequency components is identical. It’s also easy to show that cascaded linear-phase FIR filters are themselves linear phase. This means complicated multi-layer filtering schemes can be employed without this cumulative phase (timing) degradation.
The CLSLP filter synthesis algorithm is computationally efficient and fast even on a standard desktop PC. For example, the synthesis of the filter in Section 3 below, a 501-coefficient real-valued filter, takes roughly 1.6 to 3 ms in total, or about 3 µs per FIR filter coefficient.
# Using the CLSLP Algorithm
This Section provides illustrations of the practical use and characteristics of the Constrained Least-Squares Linear-Phase FIR Filter (CLSLP) synthesis algorithm which was presumably first described in reference [1]. CLSLP filters are minimum weighted square-error and possess linear-phase due to their conjugate-symmetric coefficient form. CLSLP filters are generated without a Fourier Transform and the fidelity of the synthesized filter coefficients is quite good (e.g. -150 dB stop-band in Figure 1 below). The CLSLP algorithm is also computationally efficient and so is ideal for adaptive real-time filtering applications. For example, the 501-coefficient linear-phase FIR filter below was synthesized with double-precision floating-point coefficients in 1.69 ms on a standard desktop PC. The center filter segment is an exponential-line segment type, from .1 an .4 Normalized Hz, with amplitudes of -80 dB and 0 dB at the left and right filter segment edges respectively. The other frequency segments are set to zero. Note, exponential-filter segments appear as straight lines on dB plots.

Figure 3.1: 501-Coefficient Real-Valued CLSLP [.1-.4] LPFIR Filter [EXP,ABS].
## Filter Frequency-Interval Definitions
CLSLP filter coefficients are given in Equations (32) and (33) in reference [1]. Breaking frequency up into sub-bands is intuitive as (32) and (33) are integrals over frequency. This easily accommodates unspecified frequency bands as well. By judiciously choosing the amplitude response functions used for these intervals, filter synthesis can be achieved quickly resulting in high-precision LPFIR filter coefficients.
### Frequency-Interval Types
There are currently four types of frequency intervals defined. These intervals are either linear or exponential. An exponential interval appears as a straight line on a dB plot while a linear interval appears as a straight line on a linear plot. Additionally these segments employ either absolute or relative weighting.
Absolute Weighting Type	Normal square-error
Relative Weighting Type	Normal square-error divided by the specified signal amplitude. This mode artificially boosts the fit quality of lower amplitude frequency intervals. Signal amplitudes of zero cannot be used as logarithms are employed. Use a small value instead (e.g. 1e-8).

This is the C++ data structure specification of frequency interval types

// Segment types
// [F0,F1] in frequency and [A0,A1] in amplitude for Linear Segments
// [F0,F1] in frequency and [loge(A0),loge(A1)] in amplitude for Exponential Segments
// Note that frequencies are specified in the interval [0,1) Normalized Hz.
typedef enum eSegType
{
  eExp_RelErr, // exp(B*f+A) segment, relative error
  eExp_AbsErr, // exp(B*f+A) segment, absolute error
  eLin_RelErr, // B*f+A segment, relative error
  eLin_AbsErr // B*f+A segment, absolute error
} LS_FIR_Filter;
Due to the open form of this algorithm, additional frequency-interval types can be added as needed. These four frequency-interval types are computationally efficient and have, so far anyway, sufficed in practical filter-design problems.
### Segment Parameters
Five numeric values are needed for any of the four segment types mentioned in Section 3.1.1 above. Namely X[0], X[1], Y[0], Y[1], and the weighting factor which is discussed in the next section. Here X[0] and X[1] are interval start and stop frequencies given in Normalized Hz. The filter amplitudes at the frequency-interval edges are specified as Y[0] and Y[1] (not in dB). The frequency interval type is Linear/Absolute error LS_FIR_Filter::eLin_AbsErr.
### Segment Weights
Segment weights are provided so the filter designer can change the fit quality filter sections. A value of 1 is considered normal weighting, a value of 0 means the fit error for that section is completely ignored, and a segment weight of 2 doubles the fit error. Increasing the segment weight should improve the fit in that filter segment. For example, the middle filter segment of the filter illustrated in the previous section would be specified as X[0]=.1, X[1]=.4, Y[0]=1e-4, Y[1]=1, Type=LS_FIR_Filter::eLin_AbsErr, Weight=1 .
## Using CLSLP Software
This section illustrates installing, building, then running the CLSLP filter synthesis application.
## Installation
It is fairly easy to install CLSLP and synthesize filters on any platform or context. There is no installation procedure per se. CLSLP is released here as C++20 source code and CMAKE build files. Additionally Linux command files CLEAN and BUILD_AND_RUN provide illustration of the proper command syntax. This software should build on most modern operating systems and CPU architectures. Though Linux has been used in this software’s design, MS Windows, Mac OS, and many other operating systems can be used as both the build and run environment. Build and run environments can be set separately via compiler switches in modern C++ compilers so heterogeneous computer operating systems and architectures can be integrated easily.
Executing BUILD_AND_RUN should do everything in one step. The CLEAN command isn’t really necessary unless CMAKE gets confused. CLEAN empties the build directory completely.

./CLEAN # Not really necessary --- clears subdir build/
./BUILD_AND_RUN # Build then Run the software
## CLSLP Software Distribution
CLSLP is distributed in C++ source code form. CMAKE build files are included as well as Linux script files to illustrate proper use.
### CLSLP Software Distribution
The standard CLSLP release consists of, at least, the files listed at the end of this section. The Linux GSL special function library is necessary for CLSLP LPFIR filter synthesis. FFTW and GNUPLOT are used for plot generation though neither is needed for coefficient synthesis itself.
A CLSLP release will contain at least the files specified below
- Start.cpp
- CLSLP.h
- CLSLP.cpp
- AlignedMemAlloc.h
- CLEAN
- BUILD_AND_RUN
- GENERATE_PLOTS
Header file AlignedMemAlloc.h helps provide functionality for SSE and AVX SIMD vector allocation (faster execution). This module is also the C++ main program entry-point for the software in these tests. As a local convention we use start as part of the main’s filename to identify it. Filename like Start_x.cpp are used for C++ main files in this document. For example of use see Section 4.1.2 below.
### Building Application with CMAKE
Execute the following commands in the source code where you want to store your build files. The sub-directory build is commonly used.
./CLEAN # Cleans the build directory (optional)
./BUILD_AND_RUN # Builds (CMAKE) source code and execute program
./GENERATE_PLOTS # Generate GNUPLOT plots from data files just created (optional)
### Spectral Plots
The CMAKE current directory should now contain two new PNG graphics files: the Amplitude and Phase Response graphs.
## CLSLP Filter Synthesis Applications
The only module we need to write is the start-file, or file Start_x.cpp. This is the C++ main that calls the CLSLP filter synthesis software. GenFilter is then called to synthesize the filter coefficients. The code fragment below synthesizes an LPFIR Filter with 501 real-valued double-precision coefficients into output vector OutCoefs. This vector is allocated on AVX (SIMD) memory boundaries. On Linux systems, -O3 x5pT=rAu(optimized compilation), is sufficient for basic SIMD support on CPUs that support it. Intel and AMD PC CPUs normally do support it.

// The C++ code segment that generates this 501-coefficient CLSLP filter
#include “CLSLP.h”

// Generate the CLSLP filter Coefficients into OutCoefs
const unsigned int NumFiltCoefs = 501;
CLSLP Filt;
vector<complex<double>> OutCoefs(NumFiltCoefs); // Real-valued Coefs stored in Complex

// ‘AddSymmetric’ is for Real-Valued Filter Coefficients ([0,.5] mod 1.) Normalized Hz
// ‘Add’ is for Complex-Valued Filter Coefficients ([0,1.) mod 1.) Normalized Hz
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .0, .1, 0.00, 0.00, 1 );
Filt.AddSymmetric( LS_FIR_Filter::eExp_RelErr, .1, .4, 1e-4, 1.00, 1 );
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .4, .5, 0.00, 0.00, 1 );

// Calculate the FIR Filter Coefficients into OutCoefs
Filt.GenFilter( NumFiltCoefs, OutCoefs );
## Building Filter Synthesis Software
Next we compile and link the software in the previous section into an executable. We are using CMAKE and the GNU C++ compiler build tools. The following BASH script performs the CMAKE build.

#! /bin/bash

# Generate the CMAKE files
make --fresh -S . -B build -DCMAKE_BUILD_TYPE=RELEASE -DCMAKE_VERBOSE_MAKEFILE=OFF

# Compile the C++ sources
cmake --build build
A listing of the CMAKE control file CMakeLists.txt is presented below as a convenience.

cmake_minimum_required(VERSION 3.10)

# specify the C++ standard
set(CMAKE_BUILD_TYPE Release)
set(CMAKE_CXX_STANDARD 20)
set(CMAKE_CXX_STANDARD_REQUIRED ON)
set(CMAKE_CXX_FLAGS_RELEASE "-O3 -Wall -Wextra")
set(CMAKE_CXX_FLAGS_DEBUG "-g -Wall -Wextra")
# set(CMAKE_VERBOSE_MAKEFILE ON)

# Set some basic project attributes
project (CLSLP
        VERSION 1.00
        DESCRIPTION "CLSLP Filter Synthesis")

file(GLOB SRC_FILES ${PROJECT_SOURCE_DIR}/*.cpp)

# This project will output an executable file
add_executable(${PROJECT_NAME} ${SRC_FILES})

# Include the configuration header in the build
target_include_directories(${PROJECT_NAME} PUBLIC "${PROJECT_BINARY_DIR}")

# Math includes
target_link_libraries(${PROJECT_NAME} PUBLIC "gsl")
target_link_libraries(${PROJECT_NAME} PUBLIC "gslcblas")
The following sequence of commands will perform the C++ build, then execute the synthesized code. The filter coefficients are stored in FilterCoef.dat in ASCII form.

./CLEAN # Not necessary though cleans the CMAKE build file
./BUILD_AND_RUN # Build and Run the CLSLP software
./GENERATE_PLOTS # Generates GNUPLOT plot files (Amplitude and Phase)
# FIR Filter Synthesis Examples
The functionality and use of the Constrained Least-Squares Linear-Phase CLSLP FIR Filter Synthesis algorithm is described via a series of simple examples in the following sections. These sections assume you have the software from the CLSLP Software Distribution described in Section 3.4.1 above.
## Sloped-Bandpass Filter Example
We construct a linear-phase real-valued FIR filter to pass .1 to .4 Normalized Hz and null the other frequencies. The passband starts at .1 Hz with a -80 dB response. It rises either linearly or exponentially, depending on the type of test performed, to .4 Hz with a response of 0 dB. We use a 501-tap linear-phase real-valued FIR Filter and the CLSLP algorithm to perform the filter synthesis. The amplitude spectra are calculated by performing a Discrete Fourier Transform (DFT) on a zero-padded vector of filter coefficients.
All linear-phase FIR filters have conjugate-symmetric filter coefficients by the argument given in reference [1]. Since this is a real-valued filter, conjugate-symmetric corresponds to symmetric filter coefficients here.
### Exponential/Absolute Weighted-Error Filter Segments
A linear-phase real-valued FIR filter with 501-coefficients is synthesized using the CLSLP algorithm. We are testing the exponential/absolute mode here. The synthesis takes 1572 µs or 3.14 µs per coefficient. The filter amplitude response is given in the graph below. The exponential filter segment appears as a straight line in the dB amplitude response below.
FIR filter synthesis is performed via the C++ code fragment below. The AddSymmetric function is used for real-valued filters [0-.5) and Add for complex-valued filters [0-1). AddSymmetric adds filter constraints that are conjugate-symmetric in frequency so as to guarantee real-valued filter coefficients. These coefficients are then written to the OutCoefs vector.
Figure 4.1: 501-Coefficient Real-Valued CLSLP [.1-.4] LPFIR Filter [EXP,ABS].

// The C++ code segment that generates this 501-coefficient CLSLP filter
#include “CLSLP.h”

// Generate the CLSLP filter Coefficients into OutCoefs
const unsigned int NumFiltCoefs = 501;
CLSLP Filt;
vector<complex<double>> OutCoefs(NumFiltCoefs);

// ‘AddSymmetric’ is for Real-Valued Filter Coefficients ([0,.5] mod 1.) Normalized Hz
// ‘Add’ is for Complex-Valued Filter Coefficients ([0,1.) mod 1.) Normalized Hz
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .0, .1, 0.00, 0.00, 1 ); Filt.AddSymmetric( LS_FIR_Filter::eExp_AbsErr, .1, .4, 1e-4, 1.00, 1 ); Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .4, .5, 0.00, 0.00, 1 );

// Calculate the FIR Filter Coefficients into OutCoefs
Filt.GenFilter( NumFiltCoefs, OutCoefs );
### Exponential/Relative Weighted-Error Frequency Intervals
A linear-phase real-valued FIR filter with 501-coefficients is synthesized using the CLSLP algorithm. We are testing the exponential/relative mode. This synthesis takes about 1556 µs or 3.11 µs per filter coefficient. The filter’s amplitude response is given in Figure 4.2 below. The exponential filter interval appears as a sloped-line in the dB amplitude response. The little response peak just below .1 Hz can be reduced by adding a small triangular filter design section to reduce the abrupt amplitude transition. The filter response will improve as a result.

Figure 4.2: Amplitude: 501-Coefficient Real-Valued CLSLP [.1-.4] LPFIR Filter [EXP,REL].
The code fragment below is the C++ main program used in this example.

// The C++ code segment that generates this 501-coefficient CLSLP filter
#include “CLSLP.h”

// Generate the CLSLP filter Coefficients into OutCoefs
const unsigned int NumFiltCoefs = 501;
CLSLP Filt;
vector<complex<double>> OutCoefs(NumFiltCoefs);

// ‘AddSymmetric’ is for Real-Valued Filter Coefficients ([0,.5] mod 1.) Normalized Hz
// ‘Add’ is for Complex-Valued Filter Coefficients ([0,1.) mod 1.) Normalized Hz
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .0, .1, 0.00, 0.00, 1 ); Filt.AddSymmetric( LS_FIR_Filter::eExp_RelErr, .1, .4, 1e-4, 1.00, 1 ); Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .4, .5, 0.00, 0.00, 1 );

// Calculate the FIR Filter Coefficients into OutCoefs
Filt.GenFilter( NumFiltCoefs, OutCoefs );
### Linear/Absolute Weighted-Error Filter Segments
A linear-phase real-valued FIR filter with 501-coefficients is synthesized using the CLSLP algorithm. We are testing the Linear/Absolute mode. This 501-coefficient filter can be generated in 3517 µs or 7.02 µs per coefficient. The linear slope appears as a logarithmic curve.

Figure 4.3: Amplitude: 501-Coefficient Real-Valued CLSLP [.1-.4] LPFIR Filter [LIN,ABS].
The code fragment below is the C++ main program used in this example.

// The C++ code segment that generates this 501-coefficient CLSLP filter
#include “CLSLP.h”

// Generate the CLSLP filter Coefficients into OutCoefs
const unsigned int NumFiltCoefs = 501;
LS_FIR_Filter Filt;
vector<complex<double>> OutCoefs(NumFiltCoefs);

// ‘AddSymmetric’ is for Real-Valued Filter Coefficients ([0,.5] mod 1.) Normalized Hz
// ‘Add’ is for Complex-Valued Filter Coefficients ([0,1.) mod 1.) Normalized Hz
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .0, .1, 0.00, 0.00, 1 );
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .1, .4, 1e-4, 1.00, 1 );
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .4, .5, 0.00, 0.00, 1 );

// Calculate the FIR Filter Coefficients into OutCoefs
Filt.GenFilter( NumFiltCoefs, OutCoefs );
### Linear/Relative Weighted-Error Filter Segments
A linear-phase FIR (LPFIR) filter with 501-coefficients is synthesized using the CLSLP algorithm. We are testing the linear/relative mode. The synthesis takes about 1635 µs or 3.26 µs per coefficient. The CLSLP filter amplitude response is given in Figure 4.4 below. The linear filter segment appears as a logarithmic curve in the amplitude response plot below. There is a small peak just below .1 Hz though we are close to making the -80 dB response. Adding a small triangular filter design section to reduce the abrupt amplitude transition. The filter response will improve substantially as a result. This 501-coefficient filter can be generated in 1635 µs or 3.26 µs per coefficient. The linear slope appears as a logarithmic curve.

Figure 4.4: Amplitude: 501-Coefficient Real-Valued CLSLP [.1-.4] LPFIR Filter [LIN,REL].
The code fragment below is the C++ main program used in this example.

// The C++ code segment that generates this 501-coefficient CLSLP filter
#include “CLSLP.h”

// Generate the CLSLP filter Coefficients into OutCoefs
const unsigned int NumFiltCoefs = 501;
LS_FIR_Filter Filt;
vector<complex<double>> OutCoefs(NumFiltCoefs);

// ‘AddSymmetric’ is for Real-Valued Filter Coefficients ([0,.5] mod 1.) Normalized Hz
// ‘Add’ is for Complex-Valued Filter Coefficients ([0,1.) mod 1.) Normalized Hz
Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .0, .1, 0.00, 0.00, 1 ); Filt.AddSymmetric( LS_FIR_Filter::eLin_RelErr, .1, .4, 1e-4, 1.00, 1 ); Filt.AddSymmetric( LS_FIR_Filter::eLin_AbsErr, .4, .5, 0.00, 0.00, 1 );

// Calculate the FIR Filter Coefficients into OutCoefs
Filt.GenFilter( NumFiltCoefs, OutCoefs );
## Complex-Coefficient Linear-Phase FIR (LPFIR) Filters
The filter response of a real-valued LPFIR filter possess conjugate-symmetry about 0 Hz. Therefore it suffices to specify the the amplitude response only from 0 to .5 Normalized Hz and infer the rest from the symmetry. FIR filters with complex-valued coefficients do not have conjugate symmetric filter coefficients. Therefore plots of complex-coefficient FIR filters are usually plotted from -.5 to .5 Normalized Hz.
### Example Filter 5
A linear-phase FIR filter with 1001 complex-valued coefficients is synthesized using the CLSLP algorithm. We are testing the complex-coefficient mode so amplitude plots will be displayed from -.5 to .5 Normalized Hz.

// The C++ code segment that generates this 1001-coefficient CLSLP filter
#include “CLSLP.h”

// Generate the CLSLP filter Coefficients into OutCoefs
const unsigned int NumFiltCoefs = 1001;
LS_FIR_Filter Filt;
vector<complex<double>> OutCoefs(NumFiltCoefs);

// ‘AddSymmetric’ is for Real-Valued Filter Coefficients ([0,.5] mod 1.) Normalized Hz
// ‘Add’ is for Complex-Valued Filter Coefficients ([0,1.) mod 1.) Normalized Hz Filt.Add( LS_FIR_Filter::eLin_AbsErr, .0, .05, 0.00, 0.00, 1 ); Filt.Add( LS_FIR_Filter::eExp_AbsErr, .05, .2, 1e-4, 1.00, 1 ); Filt.Add( LS_FIR_Filter::eExp_AbsErr, .2, .5, 1e-4, 1.00, 1 ); Filt.Add( LS_FIR_Filter::eExp_AbsErr, .5, .9, 1.00, 1e-4, 1 ); Filt.Add( LS_FIR_Filter::eLin_AbsErr, .9, 1.0, 0.00, 0.00, 1 );

// Calculate the FIR Filter Coefficients into OutCoefs
Filt.GenFilter( NumFiltCoefs, OutCoefs );
This filter synthesis takes 5544 µs or 5.54 µs per coefficient on a standard PC. The resultant CLSLP filter’s amplitude response is given in Figure 3.2 below.

Figure 4.5: Amplitude: Ex5 1001-Coefficient Complex-Value CLSLP LPFIR [EXP,ABS].
### Example Filter 6
This filter synthesis takes 23388 µs or 11.4255 µs per coefficient on a standard PC. The resultant CLSLP filter’s amplitude response is given in Figure 3.2 below.

Figure 1: Amplitude: Ex6 2047-Coefficient Complex-Value CLSLP LPFIR [EXP,ABS].
# Web Resources
See website http://www.wejc.com for CLSLP software information and downloads. Look for the acronym CLSLP on the initial web page. The original Asilomar paper “Constrained Least-Squares Design and Characterization of Affine Phase Complex FIR Filters”, reference [1], is included as PDF file, “Constrained Least-Squares FIR Filter Synthesis.pdf” which is included in the normal CLSLP software distribution.
The http://www.wejc.com/ website has more information on other computer science, engineering, or mathematical algorithms as well as free downloads. If you have interest in any joint-work or just want to write, feel free to write at wejc@wejc.com. We are in Washington State, United States.
# References
[1]	A. G. Jaffer and W. E. Jones, "Constrained least-squares design and characterization of affine phase complex FIR filters," Proceedings of 27th Asilomar Conference on Signals, Systems and Computers, Pacific Grove, CA, USA, 1993, pp. 685-691 vol.1, doi: 10.1109/ACSSC.1993.342607.
[2]	A. G. Jaffer and W. E. Jones, "Weighted least-squares design and characterization of complex FIR filters," in IEEE Transactions on Signal Processing, vol. 43, no. 10, pp. 2398-2401, Oct. 1995, doi: 10.1109/78.469851.
[3]	A. G. Jaffer, W. E. Jones and T. J. Abatzoglou, "Weighted least-squares design of linear-phase and arbitrary 2-D complex FIR filters," 1995 International Conference on Acoustics, Speech, and Signal Processing, Detroit, MI, USA, 1995, pp. 1256-1259 vol.2, doi: 10.1109/ICASSP.1995.480467.

CLSLP LPFIR Filter Synthesis Errata
Support Files Follow
Requires a Recent GNU or Equivalent C++ Compiler
  [C++20 Language Standard Source Code Used]

Contents
LS_FIR_Filter.h	The C++ header file for the filter synthesis software.
LS_FIR_Filter.cpp	The C++ source file for the filter synthesis software.
AlignedMemAlloc.h	SSE and AVX C++ vector allocator for faster execution on SIMD machines.
CLEAN	A BASH script that clears the CMAKE build directory.
BUILD_AND_RUN	A BASH script that performs a CMAKE build then runs the just-built program.
GENERATE_PLOTS	A BASH script that generates amplitude and phase plots, as PNG files, using GNUPLOT.
Start.cpp	The source code listing for the c++ main (where the program begins).
Constrained Least-Squares Design and Characterization of Affine Phase / Complex FIR Filters	The Asilomar paper “Constrained Least-Squares Design and Characterization of Affine Phase Complex FIR Filters” ref [1]. Detail on the general theory behind CLSLP LPFIR filters with all the requisite math. The C++ subroutines used here for CLSLP, are coded directly from the definitions in this document.